## Slide 1: Novel direct photon-to-digital conversion technique for light readouts
Lorenzo Fabris
A collaboration between ORNL and Université de Sherbrooke

## Slide 2: Applications
The main application for the technology is high-sensitivity, fast timing applications such as high-resolution, depth of interaction fast neutron radiography.
  Large panels of PSD scintillators
  Single-volume scatter cameras.
  Focus on pixel size, detector size, power, timing, cost, portability.
Not a self-contained development.
  We see this as part of and an important contribution to on-going multi-lab efforts in neutron imaging/radiography.

## Slide 3: State-of-the-art
Typically focused on portability, the field has evolved much recent years:
PMT Based – Present state-of-the-art
Simple resistive divider readout
Photon-to-Digital Converters (PDC) Based – Next state-of-the-art
All-digital, starting from the photon interaction in silicon (lowest power, very fast timing (10-100 ps), high scalability
SiPM Based – Near-future state-of-the-art
ASIC readout (lower power, better timing, compact)

## Slide 4: The Enabling Technology
PDCs are loosely based on SiPMs, but have fundamental differences that enable unprecedented performance
Bias
Amplifier, Shaper,…
ADC
Analog current sum
SiPM capacitance (=electronic noise)
Response of the SPAD is a ‘yes’ or ‘no’ (fixed charge)
Quench
Quench
DSP
Bias
The amplifier transforms charge into voltage and then BACK to digital
No D/A+A/D conversion. Everything stays digital
SiPM
PDC
SPAD
SPAD

## Slide 5: Analog Conversion Limits Performance
Analog conversion within SiPM
  Analog readout = signal distortion, limited timing and PSD performance
  More power required for BW, SNR, and signal integrity
  Large readout capacitance, SNR∝[Gain/(Noise=f(CDET))]
No analog conversion = virtually infinite SNR.
  Low power
  Fast timing (tens of ps)
  High precision
  Individual control of SPADs
10110
10000
01001
11010
11110
…
SiPM leading/trailing edge distortion induced by readout and quenching
Scintillator intrinsic response
“Binnable” digital Sum Output

## Slide 6: PDC Device
4096 Channels of electronics readout on a single chip.
61 test SPADs in a 1D row on the same chip.
The only external component needed is a “tile controller.”
PDC Chip
To 63 more chips
The SPAD array is the light-sensitive part

## Slide 7: Progress
Demonstrated functionality of SPADs and readout electronics.
Building 8x8 tile (same tile controller)
Tile controller
Temporary Interface
2x2 PDC heads

## Slide 8: Tests done
Coupled scintillator to PDC head and set up a PMT coincidence measurement. Runs proved positive light detection for the first time.
PDC1
PDC2

## Slide 9: Future Developments
What was done until now, was to demonstrate that everything works, with some limitations.
  The PDCs only have 61 SPADs (but all readout channels)
  The tile controller is an FPGA dev kit.
We want to work towards removing these limitations.

## Slide 10: Step 1: 2D SPAD arrays with 3D interconnects
The first logical step is to produce 2D SPAD arrays.
  The SPAD arrays must be integrated on top of the readout electronics using 3D vertical interconnection techniques to be further developed.
  Use a dedicated SPAD process to improve current characteristics (already comparable to commercial SiPMs, but we would like better SPADs)

## Slide 11: Step 2: system integration
The second logical step is to design the tile controller into an ASIC.
  Manage up to 8x8 arrays of SPADs
  Offer high speed serial bus to back-end.
2D SPAD Arrays
Readout Electronics
  TOP
  BOT

## Slide 12: Step 3: make panels/cube readouts