## Slide 1: Silicon MAPS Readout in ALICE and sPHENIX
J. Schambach
Oak Ridge National Laboratory
(for the ALICE ITS Upgrade & sPHENIX MVTX collaborations)

## Slide 2: ALICE Upgrades
ALICE Central Barrel Tracking from very low (100 MeV/c) to very high pt (100 GeV/c)
Silicon: r = 22 – 400 mm
Gas (TPC, TRD): r = 88 – 368 cm
 large BL2 (bending power), comparable to CMS

## Slide 3: New ITS Layout
3 Inner layers
0.3% X0
2 Middle layers
2 Outer layers
7-layer barrel, based on CMOS MAPS sensors (“ALPIDE”)
Coverage: r 22 – 400 mm, |h| ≤ 1.22
~24k pixel chips (a 12.5 G pixel camera)
~10m2 active area
1% X0
= 192 Staves in Total
Inner Barrel
Outer Barrel
48 42 30 24 20 16 12

## Slide 4: sPHENIX - MVTX
MVTX parameters: L = 271 mm
3-layer sensor barrel equivalent to ITS IB
- 48 staves, 432 chips
MVTX Readout Units, PUs
& other services
Proposal Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/
Located Outside Magnet on Platform:
Much lower Radiation than ITS
sPHENIX cost-effectively reuses the ITS electronics as built, replacing the ALICE CRU with the ATLAS FELIX backend
Modified ALICE ITS mechanics to fit it into sPHENIX

## Slide 5: ALPIDE Principle of Operation
STATE
(Latch)
STROBE
OUT_D
OUT_A
Particle hit
PIX_IN
6 µs
~2 us Peaking time
Particle hit
ΔV = Q/C : ~ 10 ns
Reset : ~1 ms
t1
t2
Threshold
Front-end acts as delay line
Sensor and front-end continuously active
Upon particle hit front-end forms a pulse with ~1-2ms peaking time (“analog delay”)
Threshold is applied to form binary pulse
Hit is latched into memory if strobe is applied during binary pulse
ultra low-power front-end circuit
40nW / pixel
Cdet~2.5 fF @ -6 Vbb
Cin~1.6fF

## Slide 6: ITS Readout Hierarchy
One READOUT UNIT for each STAVE
IL
9×960 Mb/s
ML
16×320 Mb/s
OL
28×320 Mb/s
RU
CRU
11× FLP
EPN
8× RU/CRU
24× LINKS
3× GBT LINKS/RU
RAM
NIC
3200Mb/s
110 Gb/s
110 Gb/s
110 Gb/s
100 Gb/s
<40 GB/s
DETECTOR LINKS
GBT LINKS
CRU to FLP
FLP to EPN
LTU / CTP
ALICE Timing and Trigger
LHC Bunch Clock (40.08 MHz)
Timing and Trigger messages

## Slide 7: MVTX Readout System
Power Board
Data (9x1.2Gbps), Clock, Control/Trigger
Regulated power
Readout Unit
Front End
FELIX
Back End
Data (3x4.8 Gbps)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
5-10 m twinax
GBT Optical Links
9-sensor stave
Power supplies
Power
Clock/Trigger
Interaction Region
Experimental Hall
Counting House
DAQ and Slow Control
PCIe
sPHENIX GTM

## Slide 8: Main Challenge: Expected Radiation Levels
Both TID and Fluence levels at the location of the RU are not a concern for modern micro-electronics material degradation and component reliability.
High energy hadrons are the real concern, as they can cause latch-ups in electronic components and SEU on logic devices.
Testing showed that latch-ups are not a problem, while proper design is required to mitigate SEU effects.
Position with respect to beam |  |  | Radiation levels (total) |  |  | 
r | z | Name | Total Ionizing Dose (TID) | 1 MeV neq fluence | High energy hadron flux* | Charged particle flux
[cm] | [cm] |  | [krad] | [cm-2] | [kHz cm-2] | [kHz cm-2]
2.2 | [-13.5 ÷ 13.5] | ITS L0 | 2734 | 1.7 × 1013 | 765 (770) | 890 (910)
40 | [-73.7 ÷ 73.7] | ITS L6 | 20 | 8.1 × 1011 | 3.4 (4.9) | 4.5 (6.7)
100 | 330 | RU | ≈ 5 | ≈ 1.6 × 1011 | 0.86 | 1.7
258 | [-260 ÷ 260] | TPC Out | 0.86 | 1.4 × 1011 | 0.27 (0.37) | 0.2 (0.3)
FEE

## Slide 9: Readout Unit – Top Level Diagram
Main SRAM
FPGA
FLASH
FPGA
FLASH
Memory
GBT
SCA
3 × GBTx
CAN
Bus
USB
3.0
4 × I2C
Sensors
Rad-hard by design
Rad-hard CRAM
(but SEFI possible)
Low cross section per bit (not zero!)
Hardware includes:
Xilinx Kintex Ultrascale KCU060 FPGA (main programmable logic device)
MicroSemi ProAsic3 FPGA A3PE600L (for Ultrascale scrubbing & configuration)
4 Rad Hard GBT Fiber Optic Transmitters (3.2 Gb/s each)
2 Rad Hard GBT Fiber Optic Receivers (3.2 Gb/s each)
Rad Hard Slow Controls Adapter (GBT-SCA) for monitoring and control
12 channel twinax copper interconnects to stave
Mezzanine to allow different stave configurations (“transition board”)
Power board control interface via mezzanine
CANbus interface as power board interface in case GBT is not available

## Slide 10: ITS Readout Unit
Kintex
Ultrascale
Pro
ASIC3
GBTx
GBTx
GBTx
Flash
Transition Board
I/F to sensors

## Slide 11: Hardware & Firmware Radiation Protection Measures
Radiation hard components from the LHC “Radiation Hard Optical Link Project” for communication with the control room at Gigabit speed (3.2 Gbps payload):
  “GBTx” (Transceiver) ASIC, “VTRx” opto electronics, “Slow Controls Adapter” (SCA) ASIC
Triplication of FPGA I/O’s at the hardware level for important signals
“Scrubbing” (periodic refresh of FPGA CRAM) via a flash-based FPGA
SRAM based FPGAs are sensitive to Single-Event Upsets (SEUs)
Combine scrubbing with Triple Modular Redundancy (TMR)
  TMR with majority voters of firmware modules and FSM states
  ECC protection of memories / FIFOs (1-bit correction, multi-bit detection)
Expecting improvement of Mean-Time Between Failure > 3 orders of magnitude vs unprotected designs

## Slide 12: ALICE Common Readout Unit (CRU) v2
Altera Arria 10 FPGA
Custom designed cooling
Avago Minipods:
  4x 12 TX
  4x 12 RX
48 optical outputs (MTP), 48 optical inputs (MTP)
USB Blaster II
X16, Gen3 PCIe (CFM rev 3.0); 128 Gb/s

## Slide 13: sPHENIX “BackEnd”: ATLAS FELIX
sPHENIX Timing Mezzanine
Architecture Highlights:
Xilinx Kintex Ultrascale KU115 FPGA
48 bi-directional GBT links
16 lane Gen 3 PCIe
Mezzanine site for sPHENIX timing system card
Performance:
PCIe Tx > 100Gb/s

## Slide 14: BACKUP

## Slide 15: sPHENIX DAQ Architecture
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Rack Room
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
Event Builder
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To the
RACF/HPSS
Calorimeters, INTT, MBD
TPC
Acronyms:
FEE Front End Electronics
FELIX Front End LInk eXchange
EBDC Event Buffer and Data Compressor
ATP Assembly and Trigger Processors
Buffer Box Interim storage
FEM Front End Module
DCM2 Data Collection Module
SEB Sub-Event Buffer
MVTX
MVTX Hardware:
  48 Staves
  48 FEE (Readout Units v2.0)
  6 FELIX v2.0
  6 EBDC servers

## Slide 16: ALPIDE Sensor Technology
Pixel Sensor CMOS 180 nm Imaging Process (TowerJazz)
  3 nm thin gate oxide, 6 metal layers
NA ~ 1016 cm-3
NA ~ 1013 cm-3
NA ~ 1018 cm-3
Not to scale
Key Features
29 mm x 27 mm pixel pitch, chip size 30 mm x 15 mm, 50 mm (IB) / 100 mm (OB) thick
Continuously active, ultra-low power front-end (40nW/pixel)
Ultra-low power matrix readout (< 200mW whole chip)
Global shutter: triggered acquisition or continuous readout
High speed output serial link: 1.2 Gbit/s (IB), 400 Mbit/s (OB)
zero suppression
zero suppression
zero suppression
zero suppression
Buffering and Interface
TH
COMP
AMP
ALPIDE
512 rows
1024 pixel columns
0.5 MPixel Matrix

## Slide 17: Matrix Readout
Priority encoder
Pixel front-end
512
512
STATE
RESET
512
512
STATE
RESET
0
511
…
10
VALID
SELECT
ADDR
10
VALID
SELECT
ADDR
Periphery
Data
Bias
Clock
Control
+ trigger
Pulser
Pixel front-end
Priority encoder
Pixel front-end
512
512
STATE
RESET
512
512
STATE
RESET
Pixel front-end
low-power matrix readout ~ 2mW
Pixel Matrix - Hit driven architecture
  Priority encoder sequentially provides addresses of all hit pixels present in double column
  No activity if no hit (no free running clock)  low power
28 µm
Cin ≈ 5 fF
collection electrode
2 x 2 pixel
volume
0.3 pJ / bit
Qin (MIP) ≈ 1300 e  V ≈ 40mV

## Slide 18: ALPIDE Architecture including TMR
16 double columns
32 readout regions
Region Readout (1)
128x24b DPRAM
RR (2)
RR (3)
RR (32)
Top Readout Unit
Data Management Unit
Readout Sequencing
Control Bus Logic
Configuration Registers
Pixels Config
8b DACs
11b ADC
Differential Control Port
(40 Mbps)
Bandgap +
Temp Sens
Data Transmission Unit
Driver
PLL
Serializer
Serial Out Port
(1200 Mbps / 600 Mbps/ 400 Mbps)
24b×40MHz
24b×40MHz
8b/10b
30b×40MHz
32:1 DATA MUX
Triggers
ALPIDE elements potentially SEU sensitive
1. Pixel Logic: mask and pulse registers (not protected)
Mitigation : Refresh pixel mask bits in background
2. Periphery logic: state machine, FIFO pointers, counters and configuration registers with TMR
3. Top readout unit and data management unit FIFO with Hamming protection
4. Region Readout DPRAM partially protected
format protected
hit data not protected
5. Data Transmission Unit: PLL and Serializer with TMR
1
2
3
4
5
RESET_VALUE
FF0
OUT
FF1
FF2
VOTING LOGIC
SEU_ERROR
IN
AUTO CORRECTION
Basic Triple Modular Redundancy register cell

## Slide 19: Radiation Validation: Detailed Impact
Failure mode | Affected section | Estimated occurrence in ITS operations (average MTBF) |  |  | Corrective action | Downtime per occurrence
 |  | IB | OB | Whole ITS |  | 
Sensor data lane | 1 sensor for IB ½ module for OB | 22 - 40 h | 4 - 6 h | 3 - 5 h | Self-repairing | < 1 s >
GBT data* | 1 full stave | 29 h | 10 h | 7 h | 30% self repairing, 70% reset by slow control | < 5 s >
Clock resources | 1 full stave | Negligible | Negligible | Negligible | Reset by slow control | < 5 s >
Transceiver settings | 1 sensor, IB only | > 932 h | – | – | Reset by slow control | < 5 s>
Flash memory | 1 full stave | Negligible | Negligible | Negligible | FLASH reprogramming (30 s beam off, 15m beam on) | 30 s – 15 m
1PA3 | 1 full stave | 172 h | 58 h | 43 h | Reset by slow control | < 0 s>
2DCDC power glitch | 1 full stave | 294 h | 98 h | 72 h | Power cycle | < 10 s >
* Data for the non-TMR block, the final version will use a TMR protected block. This failure mode also includes sensor control and clock failures. 1 When PA3 gets stuck, the main FPGA is not compromised, and therefore no downtime occurs. TMR of key blocks in PA3 firmware will further improve that. 2 Considering 200 RU with 8 DCDC each (20% overestimation) |  |  |  |  |  | 

## Slide 20: Server/GPU Farms for Data Acquisition and Online Processing
Data Acquisition Servers & Electronics
11 “First level Processors” (FLP)
2 CRUs & 8TB of local storage each
Storage Farm for commissioning:
  200 TB local disk server + 500 TB cloud storage
Event Processing Nodes (GPU Farms)