SNS 2020 Fitting Update
UT/ORNL n → n’ Group
5/12/2023
Cary Rock

---
Table of Integ. over ROI
Table of fits, including the error from James
PC	RAW in ROI	PLANE* in ROI (3 parameters)	PLANE* - GAUSS in ROI (3 fixed + 3 free parameters)	6-Fit in ROI (6 free parameters)	RAW - 6-Fit	James’ Errors	Total Error: James + Stat’l. in quadrature
18	2,983,763	83,532.96	161,277.52	161,277.52	2,822,485.5	1549	2320.2
19	1,975,913	74,603.50	126,493.89	126,493.89	1,849,419.1	1307	1919.4
20	1,357,524	66,850.57	106,003.61	106,003.61	1,251,520.4	2177	2469.2
21	915,234	60,965.16	89,175.18	89,175.18	826,058.8	1374	1674.2
22	637,214	55,106.60	74,571.05	74,571.05	562,642.9	963	1250.8
24	314,394	45,508.52	56,097.06	56,097.06	258,296.9	2007	2083.9
???

---
Contributions Before and After Subtraction
After the background subtraction, the slope of the fit lines becomes steeper
After the subtraction of the background, the slope of the fitted line increases.

---
Comparison of Integ. over ROI
Fits integrated over Dr. Gonzalez’ ROI
Background fits have a different slope than the neutron beam data.
5e4

---
Results of the Different Fits
FIT	F0	Error Type	F0 Error	eta	eta Error
RAW	3.31e9	Stat’l.	3.53e8	0.6771	0.004
RAW - 6-FIT	4.24e9	Stat’l. + James		0.6659
RAW - PLANE*	4.21e9	Stat’l.	3.49e8	0.6672	0.003
RAW – PLANE* - GAUSS	4.39e9	Stat’l.	3.48e8	0.6645	0.003
6-FIT only	4.42e6	James		0.8308
PLANE* only	0.52e6			0.9031
PLANE* - GAUSS only	4.42e6			0.8308

---
RESULT: RAW – 6-FIT
- The result of the fit for F0, dF0:
   F0 =
  dF0 =
- The result for eta, d(eta):
     eta =
  d(eta) =

---
sigx and sigy
sigx and sigy are free parameters in the 6-FIT

---
Future: Varying Parameters: Fixing sigx & sigy
- Constraining these to investigate influence on result
- Method: sigx is iterated over, the relevant fit parameters are determined, and the global chi2 is computed at each iteration to check the effect on results.

---
END

---
Peak – 6-Fit (Not GCP) (Same as the orange line)
Need F0, eta value for fitting – comes from
FIT	F0	eta
RAW	3314144744.7	0.6771
RAW - 6-FIT	4238496609.1	0.6659
RAW - PLANE	4208175254.4	0.6672
RAW - GCP	4388267957.5	0.6645
6-FIT only	4416081.8	0.8308
PLANE only	519028.3	0.9031
GCP only	4416081.8	0.8308