## Slide 1: Fast Neutron Imaging Detector Update
Work in Progress
3 May 2024
Paul Hausladen, Keith Vaigneur, Brandon Longmire, Matthew Heath, James Matta, Jake Daughhetee, Lorenzo Fabris

## Slide 2: Fast Neutron ”Associated Particle Imaging” (nAPI)
14.1 MeV neutrons made via the reaction
Detection of the time and position of alphas determines the time and direction of coincident neutrons (~45-degree cone)
Time and position of neutrons recorded by neutron detector
Analysis of alpha-neutron coincidences enables identification of transmitted and scattered neutrons
High data throughput DAQ and analysis software
API DT neutron generator
Alpha-particle detector
Neutron detector
(scintillator array,
readout)
Detector slider to position, execute mosaic

## Slide 3: Fast Neutron ”Associated Particle Imaging” (nAPI)
High data throughput DAQ and analysis software
API DT neutron generator
Alpha-particle detector
Time of Flight (ns)
Counts per alpha
Fission, inelastic scattering, hydrogen elastic neutrons
Transmission and small angle elastic scattering
Coincidence in space
Source and object gamma rays

## Slide 4: Laboratory Prototype
To enable field operation, first need to operate without a gantry
  Distributed DAQ (we use off-the-shelf digitizers, GbE switch, custom clock board)
  Methods to determine the detector position from data, calculate normalization for an inferred position, and stitch multiple images
Want detector with minimum non-scintillator volume
DT neutron generator
Neutron Detector

## Slide 5: Example Image
Find detector position using known alpha-coincident directions and times of flight
Calculate normalization given absolute efficiency for position and orientation of detector and corrections for relative efficiency of individual pixels
Project each image into a common plane to stich
DU
W
Pb
Steel

## Slide 6: Original Neutron Detector
Position response
Gain map
900 pixels of EJ-299-33m scintillator (yellowed with age), each 1.04 × 1.04 × 5 cm3, covering 973 cm2 area
Four quadrants of four-corner readout of 9 flat-panel PMTs (36 total) digitized by 16-channel Struck SIS-3316 waveform digitizer
Uses ~90 W of wall power (~60 W digitizer, 20 W HV), fan cooled, 43 lbs
Connections for data (Ethernet cat 6), clock (Ethernet cat 8), HV control (USB) and power

## Slide 7: Problem – Scintillator Aging
EJ-299-33m “PSD plastic” scintillator yellows with age/exposure to oxygen
Now approximately ~1/2 the light output it had in 2019, much diminished pulse shape discrimination
Preferable for new arrays to have smaller pixels

## Slide 8: ORNL Process to Build New Pixel Arrays
Scintillator ingot
Gang saw (3 cuts) into slices
Rough-cut slices
Face and diamond mill slices
Finished slices
Assemble slices
Assembled stacks
Post-cure
Gang saw into rows
Face and diamond mill rows

## Slide 9: Process to Build Pixel Arrays (Cont.)
Finished detector is 973 cm2 with 2304 pixels
Machine to finished dimensions
Dimensioned arrays
Rough arrays
Assemble rows
Polish and wrap with reflector
Post-cure
Final buffing

## Slide 10: Scaling of Fabrication Process to Smaller Pixels
Present labor cost (with no down time) is similar to cost of materials but can be additionally reduced by finishing automation of stacking (many subtleties)
We think we can build arrays with pixels as small as ~ 3 mm, but method will become limited by row breakage for smaller pixels
Array | ~ 6 mm (8x8) | ~ 3 mm* (16x16)
Scintillator | $750 | $1000
Adhesive | $100 | $200
Reflector | $15 | $30
Hours/array | 5.3 | 8.3
Stacking (% of effort) | 40% | 55%
*Requires new tooling

## Slide 11: Loading Detector
Pixel arrays optically coupled one at a time

## Slide 12: New Panel Position Response - Background
Background count shows cosmic ray MIPs reconstructing at readout quadrant centers

## Slide 13: New Panel Position Response – Cs-137 Calibration
Pulse height calibration in process, next is timing…

## Slide 14: More Granular Readout Nearly Complete
Implementing new readout (7 readout units of four-corner readout digitized by 32-channel CAEN VX2730 500 MS/s,14-bit waveform digitizer)
Will enable higher panel rates (1.5× – 2.25×)