## Slide 1: A Real-time Solution for Fast-neutron Spectroscopy
Project Number: OR24-ML-ProtonRecoilNeutronSpec-PD2Jb
James Till Matta Lorenzo Fabris Jason T. Nattress Tyler Borgwardt Michael Febbraro Juan J. Manfredi

## Slide 2: Goals and Objectives
Handheld neutron spectrometer
Efficient enough for useful spectrum after 5 min at 1m from a 106 n/s source
Low SWaP for long battery life and easy deployment
Stretch: Automatic coarse source identification
  SF, 9Be(𝛼,n), D+T, etc

## Slide 3: Introduction
Neutron energy spectra can provide a wealth of information
Current field deployable methods are… cumbersome.
Scatter cameras could measure spectra and direction
  Low efficiency
  Unweildy
Our solution will be:
  Handheld
  Mobile
  Real time

## Slide 4: Method
Combine:
  Deuterated PSD plastic scintillators
  Analog energy and PSD determination
  Low Power COTS development boards
  Well known algorithms (MLEM for spectrum decomposition)
Expected power consumption is less than10W which gives 10+ hours on battery. (And the batteries are hot-swappable)

## Slide 5: Real-time Unfolding
Counts
Counts
Neutron Energy (keV)
Neutron Energy (keV)
Fission source
PuBe
Feed-forward MLEM
  as data comes in, the algorithm will determine neutron energy for that portion and seed the next round of “unfolding” with the prior.
  Speed up convergence.
  Targeted update is on the order of a second to both acquire and determine the neutron energy spectrum
Example:
  Loop through the data in 5-second chunks (1st iteration bins and unfolds the first 5 s of data, 2nd iteration bins and unfolds the first 10 s, etc.)

## Slide 6: Current Progress
Acquired development boards, EJ276D detectors
Geant4 simulation of detector developed
  0.02% absolute efficiency for four 2”x2” @ 1m from 252Cf point source
    60,000 counts above threshold in 5 minutes with 106 source (plenty)
Testing electronic switches for suitability in gated integrators
Contract established with Cadre5 for GUI and DAQ development.
Characterization of 2”x2” and 3”x3” EJ276D detectors at LANSCE as baseline
Detector and housing frame being designed

## Slide 7: Current Progress

## Slide 8: Next Steps
Finalize and construct first revision of analog and power board.
Construct detector frame.
Design and construct housing for detectors and electronics.
Acquire and test/practice with scintillator molds at AFIT.
Develop simplified “simulator” firmware and DAQ backend components for Cadre5 to proceed with development.

## Slide 9: Conclusion
A handheld neutron spectrometer is a great boon for many applications.
  There are significantly fewer benign neutron emitters.
The project is just getting started but the path forward is clear.
The team expects great things to come!

## Slide 10
Backup

## Slide 11: Error Propagation The Basics
To first order, the covariance matrix of some vector valued function f is:
Where J is the Jacobian matrix defined as:
and Σx is the covariance matrix of the input parameters xj. (approximated as diagonal)

## Slide 12: Error Propagation Step 1
In this case the vector valued function f is:
Define the input parameters xj. To be:
Here m is the length of the response functions / input spectrum, n is the number of response functions, and p is m*n.

## Slide 13: Error Propagation Step 2
With this the Jacobian matrix is:
Plugging that into the equation for the covariance matrix gives the errors on the diagonal of the output covariance matrix.