## Slide 1: AC-LGAD Timing Detector at EIC
Satoshi YANO
(Hiroshima University)
VERTEX 2025: 33rd International Workshop on Vertex Detectors
25th – 29th Aug 2025

## Slide 2: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
BNL is selected as host
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U

## Slide 3: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
BNL is selected as host
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U

## Slide 4: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
BNL is selected as host
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
Facility performance map

## Slide 5: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
Higher Intensity
BNL is selected as host
Facility performance map

## Slide 6: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
BNL is selected as host
Facility performance map
Variable √s
Higher Intensity

## Slide 7: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
Variable √s
Higher Intensity
BNL is selected as host
Facility performance map

## Slide 8: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
Variable √s
Higher Intensity
BNL is selected as host
Facility performance map

## Slide 9: Electron Ion Collider: EIC
60 cm
105 cm
Electron-Ion Collider (EIC) is the first polarized ep and eA collider
Highly polarized beams: 70%
High luminosity: x100-1000 HERA
  1033 - 1034 cm-2s-1
Variable √s: HERA was 318GeV
  29 - 140 GeV
Variable beam species: p/d/3He…U
The EIC is a unique project, the only approved facility for the ultimate understanding of QCD
Most likely, the only novel high-energy collider in the next 15-20 years
Variable √s
Higher Intensity
BNL is selected as host
Facility performance map

## Slide 10: Important (NC) DIS Processes @ EIC
Inclusive DIS can access the parton distribution function
  Detect scattered electron to measure Q2 and xBj
Semi-inclusive DIS can reveal parton flavor
  Detect scattered electron and PID produced hadron
Exclusive DIS (non-destructive process) can access parton position from the center of nucleon
  Detect scattered electron, produced particle with PID, and scattered proton (sometimes neutron/lamda)
Inclusive DIS

## Slide 11: Important (NC) DIS Processes @ EIC
Inclusive DIS can access the parton distribution function
  Detect scattered electron to measure Q2 and xBj
Semi-inclusive DIS can reveal parton flavor
  Detect scattered electron and produced particles with PID
Exclusive DIS (non-destructive process) can access parton position from the center of nucleon
  Detect scattered electron, produced particle with PID, and scattered proton (sometimes neutron/lamda)
Inclusive DIS
Semi-inclusive DIS

## Slide 12: Important (NC) DIS Processes @ EIC
Inclusive DIS can access the parton distribution function
  Detect scattered electron to measure Q2 and xBj
Semi-inclusive DIS can reveal parton flavor
  Detect scattered electron and produced particles with PID
Exclusive DIS (non-destructive process) can access parton position from the center of nucleon
  Detect scattered electron, produced particles with PID, and scattered proton (sometimes neutron/lamda)
Inclusive DIS
Semi-inclusive DIS
Exclusive DIS

## Slide 13: Detector Design (Central)
Magnet
  New 1.7 T SC solenoid, 2.8 m bore diameter
Tracking
  Si Vertec Tracker MAPS wafer-level stiched sensor (ALICE ITS3)
  Si Tracker MAPS barrel and disks
  MPGDs (μRWELL, MMG) cylindrical and planr
Particle Identification
  high-performance DIRC
  dual RICH (aerogel + gas) (forward)
  proximity focusing RICH (backward)
  AC-LGAD TOF (barrel + forward)
EM Calorimetry
  Imaging EMCal (Barrel)
  W-powder/SciFi (Forward)
  PbWO4 crystal (backward)
Hadron Calorimetry
  FeSc (Barrel, reused from sPHENIX)
  Steel/Scint - W/Scint (backward/forward)
6.6 m
4.5 m
5 m

## Slide 14: Detector Design (Central)
Magnet
  New 1.7 T SC solenoid, 2.8 m bore diameter
Tracking
  Si Vertec Tracker MAPS wafer-level stiched sensor (ALICE ITS3)
  Si Tracker MAPS barrel and disks
  MPGDs (μRWELL, MMG) cylindrical and planr
Particle Identification
  high-performance DIRC
  dual RICH (aerogel + gas) (forward)
  proximity focusing RICH (backward)
  AC-LGAD TOF (barrel + forward)
EM Calorimetry
  Imaging EMCal (Barrel)
  W-powder/SciFi (Forward)
  PbWO4 crystal (backward)
Hadron Calorimetry
  FeSc (Barrel, reused from sPHENIX)
  Steel/Scint - W/Scint (backward/forward)
6.6 m
4.5 m
5 m

## Slide 15: Detector Design (Far-Forward)
B0 detector
Roman Pots
Off-Momentum Detectors

## Slide 16: Detector Design (Far-Forward)
B0 detector
Roman Pots
Off-Momentum Detectors

## Slide 17: Detector Design (Far-Forward)
B0 detector
Roman Pots
Off-Momentum Detectors

## Slide 18: Requirements for Timing Detectors
Excellent timing and spatial resolutions are required
  Timing for PID; spatial resolution for tracking performance
A compact detector design has been adopted to maximize acceptance and install some subsystems are installed inside the accelerator machine
  Limited installation space
The material budget must be minimized to avoid performance degradation of the other subsystems
  Most of the generated particles are a few GeV/c
The expected radiation is much smaller than that of LHC
  Radiation tolerance possibly is not big issue to use at EIC

## Slide 19: Requirements for Timing Detectors
Excellent timing and spatial resolutions are required
  Timing for PID; spatial resolution for tracking performance
A compact detector design has been adopted to maximize acceptance and install some subsystems are installed inside the accelerator machine
  Limited installation space
The material budget must be minimized to avoid performance degradation of the other subsystems
  Most of the generated particles are a few GeV/c
The expected radiation is much smaller than that of LHC
  Radiation tolerance possibly is not big issue to use at EIC

## Slide 20: Requirements for Timing Detectors
Excellent timing and spatial resolutions are required
  Timing for PID; spatial resolution for tracking performance
A compact detector design has been adopted to maximize acceptance and install some subsystems are installed inside the accelerator machine
  Limited installation space
The material budget must be minimized to avoid performance degradation of the other subsystems
  Most of the generated particles are a few GeV/c
The expected radiation is much smaller than that of LHC
  Radiation tolerance possibly is not big issue to use at EIC

## Slide 21: Requirements for Timing Detectors
Excellent timing and spatial resolutions are required
  Timing for PID; spatial resolution for tracking performance
A compact detector design has been adopted to maximize acceptance and install some subsystems are installed inside the accelerator machine
  Limited installation space
The material budget must be minimized to avoid performance degradation of the other subsystems
  Most of the generated particles are a few GeV/c
The expected radiation is much smaller than that of LHC
  Radiation tolerance possibly is not big issue to use at EIC

## Slide 22: Technology Choice: AC-LGAD
Low Gain Avalanche Detector (LGAD) is a silicon detector with a thin gain layer making high electric field
  High field increases the signal rise time and improves time resolution
  Individual layer is implemented under each electrode, so inactive is not negligible and granularity limitation is there
AC-LGAD uses AC-coupled readout with one large gain layer
  Inactive area is eliminated by one large gain layer
  Position resolution is improved by using the charge sharing
K. Nakamura et al., JPS Conf. Proc. 34, 010016 (2021)

## Slide 23: Technology Choice: AC-LGAD
Low Gain Avalanche Detector (LGAD) is a silicon detector with a thin gain layer making high electric field
  High field increases the signal rise time and improves time resolution
  Individual layer is implemented under each electrode, so inactive is not negligible and granularity limitation is there
AC-LGAD uses AC-coupled readout with one large gain layer
  Inactive area is eliminated by one large gain layer
  Position resolution is improved by using the charge sharing
K. Nakamura et al., JPS Conf. Proc. 34, 010016 (2021)

## Slide 24: AC-LGAD Time-of-Flight
The ePIC AC-LGAD TOF system is used for PID, tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of O(10 ps) and a timing resolution of O(10 um) for PID and tracking within a space of less than 10 cm in thickness are required
FFs (B0, OMD, RP) use the same technology as FTOF except geometry
Barrel-TOF (BTOF)
0.64 m
~1.4 x 2 m = ~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 25: AC-LGAD Time-of-Flight
The ePIC AC-LGAD TOF system is used for PID, tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of O(10 um) and a timing resolution of O(10 ps) for PID and tracking within a space of less than 10 cm in thickness are required
FFs (B0, OMD, RP) use the same technology as FTOF except geometry
Barrel-TOF (BTOF)
0.64 m
~1.4 x 2 m = ~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 26: AC-LGAD Time-of-Flight
The ePIC AC-LGAD TOF system is used for PID, tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of O(10 um) and a timing resolution of O(10 ps) for PID and tracking within a space of less than 10 cm in thickness are required
FFs (B0, OMD, RP) use the same technology as FTOF except geometry
Barrel-TOF (BTOF)
0.64 m
~1.4 x 2 m = ~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 27: PID Performance
Most of the produced particles are distributed below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
Decay products from D-meson in ep DIS @ √s = 141 GeV
Pion
Kaon

## Slide 28: PID Performance
Most of the produced particles are distributed below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
Decay products from D-meson in ep DIS @ √s = 141 GeV
BTOF
FTOF
BTOF
FTOF
K/p 3σ
π/K 3σ
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
Pion
Kaon

## Slide 29: PID Performance
Most of the produced particles are distributed below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
hpDIRC
BTOF
K/p 3σ
dRICH
FTOF
π/K 3σ
hpDIRC
BTOF
dRICH
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps
Pion
Kaon

## Slide 30: Sensor Design
Strip-type sensor for BTOF
  Sensor size: 32x20 mm2 (full-size) and 32x10 mm2 (half)
  Pad size: 0.05x10 mm2 (500um pitch)
    Geometry: 64x2=128 ch (full-size) and 64x1=64 ch (half-size)
  Prototype best score: σtime ~ 35 ps and σpos < 20 μm
Pixel-type sensor for FTOF and FFs
  Sensor size: 16x16 mm2
  Pad size: 0.05x0.05 mm2
    Geometry: 32x32=1024 ch
  Prototype best score: σtime ~ 20 ps and σpos ~ 20 μm
Strip-type for BTOF
  # Full-size: ~13.8k
  # Half-size: ~4.6k
  ~12 m2
  ~2.4 M channels
2 rows
64 cols

## Slide 31: Sensor Design
Strip-type sensor for BTOF
  Sensor size: 32x20 mm2 (full-size) and 32x10 mm2 (half)
  Pad size: 0.05x10 mm2 (500um pitch)
    Geometry: 64x2=128 ch (full-size) and 64x1=64 ch (half-size)
  Prototype best score: σtime ~ 35 ps and σpos < 20 μm
Pixel-type sensor for FTOF and FFs
  Sensor size: 16x16 mm2
  Pad size: 0.05x0.05 mm2
    Geometry: 32x32=1024 ch
  Prototype best score: σtime ~ 20 ps and σpos ~ 20 μm
Strip-type for BTOF
  # Full-size: ~13.8k
  # Half-size: ~4.6k
  ~12 m2
  ~2.4 M channels
2 rows
64 cols

## Slide 32: Sensor Design
Strip-type sensor for BTOF
  Sensor size: 32x20 mm2 (full-size) and 32x10 mm2 (half)
  Pad size: 0.05x10 mm2 (500um pitch)
    Geometry: 64x2=128 ch (full-size) and 64x1=64 ch (half-size)
  Prototype best score: σtime ~ 35 ps and σpos < 20 μm
Pixel-type sensor for FTOF and FFs
  Sensor size: 16x16 mm2
  Pad size: 0.05x0.05 mm2 (500um pitch)
    Geometry: 32x32=1024 ch
  Prototype best score: σtime ~ 20 ps and σpos ~ 20 μm
Strip-type for BTOF
  # Full-size: ~13.8k
  # Half-size: ~4.6k
  ~12 m2
  ~2.4 M channels
Pixel-type for FTOF
  # Sensor: ~3.6k
  ~1.1 m2
  ~3.6 M channels
2 rows
64 cols
32 rows
32 cols

## Slide 33: Sensor Design
Strip-type sensor for BTOF
  Sensor size: 32x20 mm2 (full-size) and 32x10 mm2 (half)
  Pad size: 0.05x10 mm2 (500um pitch)
    Geometry: 64x2=128 ch (full-size) and 64x1=64 ch (half-size)
  Prototype best score: σtime ~ 35 ps and σpos < 20 μm
Pixel-type sensor for FTOF and FFs
  Sensor size: 16x16 mm2
  Pad size: 0.05x0.05 mm2 (500um pitch)
    Geometry: 32x32=1024 ch
  Prototype best score: σtime ~ 20 ps and σpos ~ 20 μm
Strip-type for BTOF
  # Full-size: ~13.8k
  # Half-size: ~4.6k
  ~12 m2
  ~2.4 M channels
Pixel-type for FTOF
  # Sensor: ~3.6k
  ~1.1 m2
  ~3.6 M channels
2 rows
64 cols
32 rows
32 cols
Details were presented by Simone on Tuesday

## Slide 34: ASIC
Different ASICs are used for Strip-type and Pixel-type
  Detector capacitance is different from strip and pixel pad
FCFD for Strip-type:
  TOA + ADC（65 nm process）
  Detector capacitance target: <15pF
  Dynamic range: 5 ~ 40 fC
  Power consumption: 2~4 mW/ch
  64 x 2 = 128 ch
  Timing jitter (analog): 10 ~ 20 ps
EICROC for Pixel-type:
  TOA + ADC（130 nm process）
  Detector capacitance target: 1~5 pF
  Dynamic range: 1~50 fC
  Power consumption: <2 mW/ch
  32 x 32 = 1024 ch
  Timing jitter (analog): 10 ~ 20 ps

## Slide 35: ASIC
Different ASICs are used for Strip-type and Pixel-type
  Detector capacitance is different from strip and pixel pad
FCFD for Strip-type:
  TOA + ADC（65 nm process）
  Detector capacitance target: <15pF
  Dynamic range: 5 ~ 40 fC
  Power consumption: 2~4 mW/ch
  64 x 2 = 128 ch
  Timing jitter (analog): 10 ~ 20 ps
EICROC for Pixel-type:
  TOA + ADC（130 nm process）
  Detector capacitance target: 1~5 pF
  Dynamic range: 1~50 fC
  Power consumption: <2 mW/ch
  32 x 32 = 1024 ch
  Timing jitter (analog): 10 ~ 20 ps
FCFDv1

## Slide 36: ASIC
Different ASICs are used for Strip-type and Pixel-type
  Detector capacitance is different from strip and pixel pad
FCFD for Strip-type:
  TOA + ADC（65 nm process）
  Detector capacitance target: <15pF
  Dynamic range: 5 ~ 40 fC
  Power consumption: 2~4 mW/ch
  64 x 2 = 128 ch
  Timing jitter (analog): 10 ~ 20 ps
EICROC for Pixel-type:
  TOA + ADC（130 nm process）
  Detector capacitance target: 1~5 pF
  Dynamic range: 1~50 fC
  Power consumption: <2 mW/ch
  32 x 32 = 1024 ch
  Timing jitter (analog): 10 ~ 20 ps
FCFDv1

## Slide 37: ASIC
Different ASICs are used for Strip-type and Pixel-type
  Detector capacitance is different from strip and pixel pad
FCFD for Strip-type:
  TOA + ADC（65 nm process）
  Detector capacitance target: <15pF
  Dynamic range: 5 ~ 40 fC
  Power consumption: 2~4 mW/ch
  64 x 2 = 128 ch
  Timing jitter (analog): 10 ~ 20 ps
EICROC for Pixel-type:
  TOA + ADC（130 nm process）
  Detector capacitance target: 1~5 pF
  Dynamic range: 1~50 fC
  Power consumption: <2 mW/ch
  32 x 32 = 1024 ch
  Timing jitter (analog): 10 ~ 20 ps
FCFDv1
EICROC0

## Slide 38
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
K/p
π/K

## Slide 39
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
K/p
π/K

## Slide 40
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
K/p
π/K
Best scenario (Upper edge)
ToyMC @ y=0
Electronics jitter: 5 ps
Start time: 20 ps
Track length: 0.1 mm

## Slide 41
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
K/p
π/K
Worst scenario (Lower edge)
ToyMC @ y=0
Electronics jitter: 15 ps
Start time: 25 ps
Track length: 10 mm

## Slide 42
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
hpDIRC limit for 3σ K/p sep. of
imaging mode
hpDIRC limit for 3σ π/K sep. of imaging mode
K/p
π/K
ToyMC @ y=0

## Slide 43
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Current best performance
σsensor ~ 35 ps
Sensor Performance v.s. PID Performance
K/p
π/K
ToyMC @ y=0
hpDIRC limit for 3σ K/p sep. of
imaging mode
hpDIRC limit for 3σ π/K sep. of imaging mode

## Slide 44
Δp ~ 0.5 GeV/c
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps
Sensor Performance v.s. PID Performance
K/p
π/K
ToyMC @ y=0
hpDIRC limit for 3σ K/p sep. of
imaging mode
hpDIRC limit for 3σ π/K sep. of imaging mode

## Slide 45
Δp ~ 0.5 GeV/c
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps
Sensor Performance v.s. PID Performance
K/p
π/K
ToyMC @ y=0
hpDIRC limit for 3σ K/p sep. of
imaging mode
hpDIRC limit for 3σ π/K sep. of imaging mode

## Slide 46
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Sensor Performance v.s. PID Performance
K/p
π/K
No overlap with hpDIRC for K/p separation
ToyMC @ y=0
hpDIRC limit for 3σ K/p sep. of
imaging mode
hpDIRC limit for 3σ π/K sep. of imaging mode

## Slide 47: Detector Design Concept
BTOF
Back-side
Front-side

## Slide 48: Detector Design Concept
FTOF
BTOF
Back-side
Front-side
Module

## Slide 49: BTOF Stave
Front-side
Back-side
Half-Stave
48 (full-size) + 32 (half-size) sensors
Fold up
64 FCFDs

## Slide 50: BTOF Stave
Front-side
Back-side
Half-Stave = 8 Stavelets
48 (full-size) + 32 (half-size) sensors
Fold up
64 FCFDs
160 [mm]
FPC
Interposer
Sensor
ASIC
600 [mm]
Module (Stavelet)

## Slide 51: BTOF Stave
Front-side
Back-side
48 (full-size) + 32 (half-size) sensors
Fold up
64 FCFDs
160 [mm]
FPC
Interposer
Sensor
ASIC
600 [mm]
Module (Stavelet)
x 8 x 3 x 2 x 288
=13824
(2 x 8) x 2 x 288
=4608
Half-Size
Full-Size
Half-Stave = 8 Stavelets

## Slide 52: BTOF Stave
Front-side
Back-side
160 [mm]
Services
PB + RB
lpGBT
VTRx
x4
FPC
Interposer
Sensor
ASIC
DCDC
600 [mm]
Fold up
Module (Stavelet)
xα
x 8 x 3 x 2 x 288
=13824
(2 x 8) x 2 x 288
=4608
Full-Size
Half-Size
48 (full-size) + 32 (half-size) sensors
64 FCFDs
Half-Stave = 8 Stavelets
Backend

## Slide 53: BTOF Stave
Front-side
Back-side
160 [mm]
Services
PB + RB
lpGBT
VTRx
x4
FPC
Interposer
Sensor
ASIC
DCDC
600 [mm]
Fold up
Module (Stavelet)
xα
x 8 x 3 x 2 x 288
=13824
(2 x 8) x 2 x 288
=4608
Full-Size
Half-Size
48 (full-size) + 32 (half-size) sensors
64 FCFDs
Half-Stave = 8 Stavelets
~200 lines in FPC
Backend

## Slide 54: BTOF Stave
Front-side
Back-side
160 [mm]
Services
PB + RB
lpGBT
VTRx
x4
FPC
Interposer
Sensor
ASIC
X/X0 3~5 % (including support structure)
DCDC
600 [mm]
Fold up
Module (Stavelet)
xα
x 8 x 3 x 2 x 288
=13824
(2 x 8) x 2 x 288
=4608
Full-Size
Half-Size
48 (full-size) + 32 (half-size) sensors
64 FCFDs
Half-Stave = 8 Stavelets
~200 lines in FPC
Backend

## Slide 55: BTOF Stave
Front-side
Back-side
160 [mm]
Services
PB + RB
lpGBT
VTRx
x4
FPC
Interposer
Sensor
ASIC
X/X0 3~5 % (including support structure)
DCDC
Backend
600 [mm]
Fold up
Module (Stavelet)
xα
INTT BEX @ sPHENIX
122 lines in 1350 mm long with 0.7% X/X0
48 (full-size) + 32 (half-size) sensors
64 FCFDs
Half-Stave = 8 Stavelets
~200 lines in FPC

## Slide 56: FTOF Module
16 [mm]
3 module
6 module
7 module

## Slide 57: FTOF Module
16 [mm]
45 [mm]
4 Sensors + 4 ASICs
= Moodule
34.2 [mm]
ASIC
Sensor
3 module
6 module
7 module

## Slide 58: FTOF Module
16 [mm]
103 [mm]
DCDC
DCDC
DCDC
lpGBT
VTRx
Backend
Readout Bord
Flop over
45 [mm]
Power Bord
4 Sensors + 4 ASICs
= Moodule
34.2 [mm]
Service Hybrid (3 modules)
3 module
6 module
7 module
X/X0 7~8 % (including support structure)
ASIC
Sensor

## Slide 59: FTOF Module
16 [mm]
103 [mm]
DCDC
DCDC
DCDC
lpGBT
VTRx
Backend
Readout Bord
Flop over
Power Bord
Service Hybrid (3 modules)
X/X0 7~8 % (including support structure)
Mechanical, integration, and cooling is similar to ETL @ CMS
3 module
6 module
7 module

## Slide 60: Conclusion
The EIC is a unique project, the only approved facility for the ultimate understanding of QCD
AC-LGAD timing detector provides excellent timing and spatial resolution in a small space and is used for PID, tracking, and background rejection
AC-LGAD prototype already meets our requirement
Design of the detector system is underway by gathering technologies used at previous/current experiments

## Slide 61: Conclusion
The EIC is a unique project, the only approved facility for the ultimate understanding of QCD
AC-LGAD timing detector provides excellent timing and spatial resolution in a small space and is used for PID, tracking, and background rejection
AC-LGAD prototype already meets our requirement
Design of the detector system is underway by gathering technologies used at previous/current experiments

## Slide 62: Conclusion
The EIC is a unique project, the only approved facility for the ultimate understanding of QCD
AC-LGAD timing detector provides excellent timing and spatial resolution in a small space and is used for PID, tracking, and background rejection
AC-LGAD prototype already meets our requirement
Design of the detector system is underway by gathering technologies used at previous/current experiments

## Slide 63: Conclusion
The EIC is a unique project, the only approved facility for the ultimate understanding of QCD
AC-LGAD timing detector provides excellent timing and spatial resolution in a small space and is used for PID, tracking, and background rejection
AC-LGAD prototype already meets our requirement
Design of the detector system of AC-LGAD is underway by gathering technologies used at previous/current experiments

## Slide 64: Backup slides

## Slide 65: Demonstrator Project
Demonstrate the assembly procedure and study the thermal characteristic of a stavelet
First prototype of interposer board produced
Using non working full size detectors from the HPK production
Since no full-size ASIC available yet, using Si heaters
Fully load a double-sided stavelet with active pipe cooling and check thermal dissipation in prototype

## Slide 66: Power Board + Readout Board
Readout Board (RB)
  Each RB includes
    lpGBT for high-speed data transmission
    VTRx+ optical transceiver
    MUX64 multiplexer for monitoring
Power Board (PB)
  Each PB consists of three CERN bPOL48V DC-DC converters to provide the necessary voltages for powering the RB and ASICs
  The PB connects to the RB through board-to-board connectors
500 kHz interaction case
 | BTOF | FTOF
Data Rate | 7 Gbps | 18 Gbps
Power Budget | ~15 kW | ~7 kW
Prototyping for FTOF is ongoing and it will be extended to BTOF version

## Slide 67: BTOF and FTOF Design
FTOF
BTOF