## Slide 1: Progress with precise on-pixel time stamping and event selection with Timepix4 and Picopix
M. Campbell1, X. Llopart,
on behalf of the Medipix4 Collaboration and the Picopix design team
CERN, EP Department
1211 Geneva 23
Switzerland
1 Honorary Professor at Glasgow University
Notes: I am going to talk about the hybrid pixel detector readout chips that have been designed at CERN in the framework of the Medipix2 and 3 collaborations.

## Slide 2: Hybrid Silicon Pixel Detectors
Noise-hit free images possible (high ratio of threshold/noise)
Standard CMOS can be used (follow industry)
Sensor material can be changed (Si, GaAs, CdTe..)
Semiconductor sensor can be replaced by a gas gain grid or MCP
Permits novel fast sensor topologies
Notes: Mention signal generation Add X section?

## Slide 3: Outline
The Medipix and Timepix family timeline
Timepix4 description
Timepix4 characterisation
Progress with Through Silicon Via processing
Picopix
Some personal observations
Summary and Conclusion

## Slide 4
Medipix2 (1999 -> ) | Medipix3 (2005 -> ) | Medipix4 (2016 -> )
Albert-Ludwig Universität Freiburg, Germany | Albert-Ludwig Universität Freiburg, Germany | CEA, Paris, France
CEA, Paris, France | AMOLF, Amsterdam, The Netherlands | CERN, Geneva, Switzerland
CERN, Geneva, Switzerland | Brazilian Light Source, Campinas, Brazil | DESY-Hamburg, Germany
Czech Academy of Sciences, Prague, Czechia | CEA, Paris, France | Diamond Light Source, England, UK
ESRF, Grenoble, France | CERN, Geneva, Switzerland | IEAP, Czech Technical University, Prague, Czeciah
IEAP, Czech Technical University, Prague, Czech Republic | DESY-Hamburg, Germany | IFAE, Barcelona, Spain
IFAE, Barcelona, Spain | Diamond Light Source, England, UK | JINR, Dubna, Russian Federation
Mid Sweden University, Sundsvall, Sweden | ESRF, Grenoble, France | NIKHEF, Amsterdam, The Netherlands
MRC-LMB Cambridge, England, UK | IEAP, Czech Technical University, Prague, Czech Republic | University of California, Berkeley, USA
NIKHEF, Amsterdam, The Netherlands | KIT/ANKA, Forschungszentrum Karlsruhe, Germany | University of Canterbury, Christchurch, New Zealand
University of California, Berkeley, USA | Mid Sweden University, Sundsvall, Sweden | University of Geneva, Switzerland
Universität Erlangen-Nurnberg, Erlangen, German | NIKHEF, Amsterdam, The Netherlands | University of Glasgow, Scotland, UK
University of Glasgow, Scotland, UK | Univesridad de los Andes, Bogota, Columbia | University of Houston, USA
University of Houston, USA | University of Bonn, Germany | University of Maastricht, The Netherlands
University and INFN Section of Cagliari, Italy | University of California, Berkeley, USA | University of Oxford, England, UK
University and INFN Section of Pisa, Italy | University of Canterbury, Christchurch, New Zealand | INFN, Italy
University and INFN Section of Napoli, Italy | Universität Erlangen-Nurnberg, Erlangen, German | Chinese Spallation Neutron Source, Dongguan City,China
 | University of Glasgow, Scotland, UK | Brazilian Light Source, Campinas, Brazil
 | University of Houston, USA | Philippines Nuclear Research Institute, Manila, Philippines
 | University of Leiden, The Netherlands | Czech Academy of Sciences, Prague, Czech Republic
 | Technical University of Munich, Germany | Univeristy of Tennessee, Knoxville, USA
 | VTT Information Technology, Espoo, Finland | 

## Slide 5: Commercial Partners
COLLABORATION NAME | Medipix2 |  |  | Medipix3 |  | Medipix4 | 
ASICS | Medipix2 | Timepix | Timepix2 | Medipix3 | Timepix3 | Medipix4 | Timepix4
ADVACAM s.r.o., CZ | X | X | X | X | X |  | X
Amsterdam Scientific Instruments, NL | X | X |  | X | X |  | X
Kromek, UK | X | X | X |  | X |  | 
Malvern-Panalytical, NL | X | X |  | X |  |  | 
MARS Bio Imaging, New Zealand |  |  |  | X |  |  | 
PITEC, Brazil |  |  | X | X |  |  | X
Quantum Detectors, UK |  |  |  | X |  |  | X
Sequent Logic, USA |  |  |  |  |  |  | X
Sydor Technologies, USA |  |  |  |  |  |  | X
Thermo Fischer Scientific, CZ |  |  |  |  |  |  | X
X-ray Imaging Europe, Germany | X | X |  |  |  |  | 
X-spectrum, Germany |  |  |  | X |  |  | X
X = commercial licensee X = R and D licensee

## Slide 6: Motivation for Medipix/Timepix Developments
Hybrid pixel detectors for the LHC are designed to do one thing extremely well
  Tag each traversing particle to one bunch crossing (25ns)
  On-chip (or on-pixel) hit buffering and selection (only triggered events are read out)
  Tolerate extreme radiation environment
The Medipix/Timepix chips were intended to use the same technology for other applications
  Not so Application Specific Integrated Circuit
The Medipix family aims primarily at high flux spectroscopic X-ray imaging
The Timepix family is better suited to detecting single particles
The experience gathered has led to innovative solutions for the LHC machine and experiments (VELOpix, Picopix etc)

## Slide 7: The Medipix and Timepix ASICs - Timeline
Collaboration | 2003 | 2006 | 2013 | 2014 | 2017 | 2018 | 2020 | 2022 | 2025?
Medipix2 | Medipix2 | Timepix |  |  |  | Timepix2 |  |  | 
Medipix3 |  |  | Medipix3 | Timepix3 |  |  |  |  | 
Medipix4 |  |  |  |  |  |  | Timepix4 | Medipix4 | 
LHCb |  |  |  |  | VELOpix |  |  |  | Picopix
Medipix chips aim at energy sensitive photon counting and typically use frame-based readout
Timepix chips are more oriented towards single particle detection

## Slide 8: The Medipix and Timepix ASICs - Timeline
Medipix chips aim at energy sensitive photon counting and typically use frame-based readout
Timepix chips are more oriented towards single particle detection
This talk will focus on the Timepix4 and Picopix chips
Collaboration | 2003 | 2006 | 2013 | 2014 | 2017 | 2018 | 2020 | 2021 | 2026?
Medipix2 | Medipix2 | Timepix |  |  |  | Timepix2 |  |  | 
Medipix3 |  |  | Medipix3 | Timepix3 |  |  |  |  | 
Medipix4 |  |  |  |  |  |  | Timepix4 | Medipix4 | 
LHCb |  |  |  |  | VELOpix |  |  |  | Picopix

## Slide 9: Timepix4
 |  |  | Specifications
Technology |  |  | 65nm – 10 metal
Pixel Size |  |  | 55 x 55 µm
Pixel arrangement |  |  | 4-side buttable 512 x 448
Sensitive area |  |  | 6.94 cm2
Readout Modes | Data driven (Tracking) | Mode | ToT and ToA
 |  | Event Packet | 64-bit
 |  | Max rate | <3.58 Mhits/mm2/s
 |  | Max pix rate | 10.6kHz/pixel
 | Frame based (Imaging) | Mode | CRW: PC (8 or 16-bit)
 |  | Frame | Full Frame (without pixel addr) CRW (8-bit / 16-bit) Up to 44 KHz frame @8b
 |  | Max count rate | ~800 Ghits/cm2/s
TOT energy resolution |  |  | < 1Kev
Time resolution (bin size) |  |  | ~200ps
Readout bandwidth |  |  | ≤163 Gbps (16 x 10.24 Gbps)
Target global minimum threshold |  |  | <500 e-

## Slide 10: Timepix4 Floorplan
29960 µm
TSVs
TSVs
24700 µm
q
28160 µm (512 x 55 µm)
24640 µm (448 x 55 µm)
TSV_TOP (460 um)
WB_TOP (900 um)
TSV_MID (920 um)
TSV_BOT (460 um)
WB_BOT (900 um)
13158.4 µm
(256 x 51.4 µm)

## Slide 11: Timepix4 Bottom left detail
BOTTOM Periphery
BOTTOM Matrix
BOTTOM
WB Extender
Dicing lane #1
Dicing lane #2
460 µm

## Slide 12: Tiling larger areas
Wire Bonding
Target to build large area detectors by combining smaller modules.
The through-silicon vias (TSVs) is the key technology for this paradigm shift.
Timepix4s use on-chip interposer for bump to pixel redistribution layer (RDL).
The detector is fully sensitive: even above the peripheral circuit and I/O pads.
ASIC
PCB
Sensor
FC
FC
BGA

## Slide 13: Timepix4 Pixel Schematic
Global threshold
Front-end
Leakage
Current
compensation
Preamp
Input
pad
1 pixel
VCO
@640MHz
Super pixel
Control
voltage
8 pixels
640MHz
TpA
TpB
TestBit
MaskBit
Front-end
Counters
&
Latches
Time stamp
14-bits
Synchronizer
&
Clock gating
OP Mode
5-bit Local
Threshold
~50mV/ke-
2.5fF
3fF
Sync
Readout
Data out
to EOC
8-bits
clock
(40MHz)
8-bits
4
8-bits
ADB
32 pixels
8
Clock
local
 | bits
ADDR | 9
ToA | 16
ufToA_r | 4
ufToA_f | 4
fToA_r | 5
fToA_f | 5
ToT | 12
Pileup | 1
SPG

## Slide 14: Pixel Operation in TOA & TOT [DD]
Preamp Out
Disc Out
Clk (40MHz)
VCO Clk (640MHz)
TOT Clk (40MHz)
TOA (16-bit)
Global TOA (16-bit)
UFTOA_Start (4-bits)
UFTOA_Stop (4-bits)
65534
X
TOA (16 bits)=65534
Tpeak < 25ns
TOT (10 bits) =4
65535
0
2
3
4
65534
65533
1
FTOA_R (4 bits)=7
FTOA_F (4 bits)=11
0
X
8
X

## Slide 15: Full digital double column DLL [448 dDLL: 224 Top Matrix and 224 Bottom Matrix]
ADB
coarse
delay
section
fine
delay
section
14
15
ctrl_fine
in
out
output buffer
ctrl_coarse
iWoRID 2018
X. Llopart et al 2019 JINST 14 C01024
Timepix4 ~23 mW/cm2 @40MHz clock with a 100 psrms
Timepix3 ~100mW/cm2 @40MHz clock with ~1.2ns skew
Dynamic digital power consumption is distributed across the clock period
Chart: Delay code
BCspectre | 0.27757 | 0.33289 | 0.3165 | 0.37181 | 0.73063 | 0.78595 | 0.77124 | 0.82655
TCspectre | 0.40701 | 0.47999 | 0.46629 | 0.53927 | 1.102 | 1.175 | 1.1647 | 1.2376
WCspectre | 0.68415 | 0.79703 | 0.78717 | 0.90004 | 1.9021 | 2.0149 | 2.0124 | 2.1253
Measured in Timepix4v2

## Slide 16: Analog (static) power supply distribution
 | Total I (chip) |  | 2 WB | 3 TSV
Nominal Analog Power [10 µA/pixel] | ~2300 mA | Vdrop [VDDA-GNDA] | 19.6 mV | 6.9 mV
 |  | Imax pad | 60 mA | 57 mA
Low Analog Power [1 µA/pixel] | ~230 mA | Vdrop [VDDA-GNDA] | 1.96mV | 0.69mV
 |  | Imax pad | 6 mA | 5.7 mA
2 sets of wire bonds
With TSVs

## Slide 17: Timepix4 submissions
Timepix4v2
4 FEOL + 4 BEOL masks changed
19 wafers received
Q2 2021
TDC and High speed links working as expected
Further improvement in RDL shielding in peripheries
Chip at its production version
Timepix4v0
~17 FTEE
Full mask engineering run
6 wafers received
Q4 2019
Excess noise coupling from peripheries to FE
640 MHz clock in edge peripheries
VCO not oscillating at nominal frequency
Chip is operational
Timepix4v1
4 BEOL masks changed
Small test VCO chip
6 wafers received
Q3 2020
VCO not oscillating at nominal frequency
Improved RDL shielding in peripheries
640MHz in peripheries recovered
Timepix4v3
2 BEOL masks changed
25 wafers received
+ 50 wafers (2024)
Q3 2022
Larger IO Pads
Chip at its production version

## Slide 18: Analog pixel summary measureament
Preliminary results
FE settings in nominal power mode
Pixels on top of peripheries not described here
Ctest=3.2 fF assumed
 | Electron collection |  | Holes collection |  | 
 | High Gain | Low Gain | High Gain | Low Gain | Log Gain
Pixel gain | ~35.8mV/ke- | ~20.5mV/ke- | ~34.5mV/ke- | ~20.5mV/ke- | ~20.5mV/ke-
Gain variation | <2% | <2% | <2% | <2% | <2%
ENC | ~65 e-rms | ~80 e-rms | ~65 e-rms | ~80 e-rms | ~80 e-rms
Amplitude Linearity | < 7 ke- | < 12 ke- | < 7ke- | < 13 ke- | < 7ke-
Threshold Eq | < 35 e-rms | < 60 e-rms | < 35 e-rms | < 60 e-rms | tbd
Min Threshold | < 450 e- | < 650 e- | < 450 e- | < 650 e- | tbd
TOT Energy resolution (Si) (@ Qin < ~2ke-) | <1.5 keVFWHM | tbd | <1.5 keVFWHM | tbd | tbd
TOA bin size | ~160 ps (instead of 195 ps) |  |  |  | 
TOA resolution (@Qin>~7ke-) | <100 psrms | tbd | <100 psrms | tbd | tbd

## Slide 19: Timepix4v2 ENC
Chart: [e-]

## Slide 20: Timepix4v1/2: Number of Noisy pixels (>1 count) in DD
Chart: Thr[e-]
| 2000 | 1950 | 1900 | 1850 | 1800 | 1750 | 1700 | 1650 | 1600 | 1550 | 1500 | 1450 | 1400 | 1350 | 1300 | 1250 | 1200 | 1150 | 1100 | 1050 | 1000 | 950 | 900 | 850 | 800 | 750 | 700 | 650 | 600 | 550
DD-TPIX4v1 (TOA ON) 0.1s | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10 | 11 | 11 | 14 | 17 | 22 | 26 | 35 | 43 | 54 | 66 | 88 | 102 | 129 | 185 | 237 | 348 | 478 | 820 | 1250 | 2996 | 27343
DD-TPIX4v1 (TOA OFF) 0.1s | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 9 | 10 | 11 | 12 | 16 | 17 | 22 | 25 | 28 | 34 | 39 | 44 | 49 | 56 | 64 | 82 | 98 | 134 | 174 | 290 | 536 | 1939
DD-TPIX4v2 (TOA ON) 0.1s | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 6 | 6 | 9 | 9 | 14 | 18 | 25 | 28 | 34
DD-TPIX4v2 (TOA OFF) 0.1s | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 5 | 9 | 11 | 13 | 15 | 23 | 31 | 39

## Slide 21: Equalization matrix [PC24bit mode, e- collection high gain]
All pixels responding (448x512)
11 pixels masked
No observable systematic across matrix

## Slide 22: Timepix4 2D VCO distribution (MHz)
Measured VCO oscillation frequency in Timepix4 using on chip Test Pulse circuitry
Most of measured dispersion across chip due to power supply distribution (VCO design sensitivity of 1MHz/mV)
VCO Calibration is required to get to the designed time resolution (~60psrms)
Large improvement expected with TSVs
700
650
600
600 700

## Slide 23: Timepix4 assembly (300mm Si sensor)

## Slide 24: Timepix4 – works! 
10 s exp. 90Sr
Threshold ~ 800e-
6.1 M packets @ 5 Gbps
5 ms timeslice

## Slide 25: Photon counting image Timepix4
Timepix4 paper:
X. Llopart et al 2022 JINST 17 C01044

## Slide 26: Timing resolution measurements of Timepix4V2 assembly with picosecond laser setup
Setup:
  Timepix4v2 bonded to a 100 μm n-on-p Si detector:
    Biased at -150 V
    Metallization with holes pattern
  Pulsed Diode Laser PDL 800-B:
    1060 nm
    Trigger simultaneously sent to laser and Timepix4 Trigger input
σ = 1.4 pixel = 77 μm
most of the charge is released in 4-5 pixels
Wide range of released charge covered
R.Bolzonella (INFN Ferrara)
Measurement:
  After TOT timewalk correction and VCO calibration:
    Single pixel resolution of 111 ± 1 ps
    Cluster timing resolution of σToAAvg = 49 ± 1 ps

## Slide 27: Timepix4 telescope
K. Akiba et al. arXiv:2503.15207v1 [hep-ex] 19 Mar 2025

## Slide 28: Timepix4 telescope
K. Akiba et al. arXiv:2503.15207v1 [hep-ex] 19 Mar 2025

## Slide 29: Timewalk correction – all pixels
K. Akiba et al. arXiv:2503.15207v1 [hep-ex] 19 Mar 2025
Single plane (100 mm sensor)
Temporal resolution 175 ps

## Slide 30: Timepix4 telescope summary
K. Akiba et al. arXiv:2503.15207v1 [hep-ex] 19 Mar 2025
Telescope was operated at 2 x 106 particles per second (highest possible at CERN SPS) with <1% loss in efficiency

## Slide 31: Timepix4 Wafer Probing
Tested > 35 Wafers
Average yield of >85%
Jerome Alozy et al.

## Slide 32: Timepix4 Through-Silicon-Via (TSV)
Redistribution Layer + UBM designed at CERN
Launched a multisite production (2 European and 1 Asian)
  Using Timepix4V0, V1 (as setup wafers) V2 and V3 as “gold” wafers
  Expected to receive ~300 Timepix4v3 with TSVs this month
Rear side view of TPIX4 wuth RDL
Naked finger board
Finger board with TSV processed Timepix4
Fran Piernas, Jerome Alozy et al.

## Slide 33
Examples of applications outside of HEP
X-ray materials analysis with diffraction
Photon counting cameras at synchrotrons
Time resolved cameras at synchrotrons
X-ray non-destructive testing
X-ray dosimetry - dosepix chip development
Waste sorting using X-rays
Low Energy Electron Microscopy
Transmission electron microscopy
Dose deposition tracking in hadron therapy
Numerous satellite systems dedicated to space weather observation

## Slide 34: The Picopix project
PicoPix is a large-scale hybrid pixel tracking particle detector designed in 28nm CMOS:
Large area  3-side buttable with 384 x 256 pixel array
Spatial resolution  square pixel size of 50 μm
Time measurements  <50 psrms per Hybrid (ASIC + Sensor)
Radiation hardness  < 1 Grad with full TMR (Triple Modular Redundancy) logic design
Data reduction  On-chip programmable event clustering, veto, filtering and sorting
Event rate  Up to 96 events/chip/25ns  ≤3.84∙109 events/chip
High speed serializer  Data-driven readout with up-to 4 x 25.6 Gbps fast links
Design Approach:
Built from gained experienced from previous hybrid pixel detectors tracking detectors designed in EP-ESE-ME:
  Timepix (2007)  Timepix3 (2013)  Velopix1 (2016)  Timepix4 (2020)
  CERN and Nikhef design team
Directly profiting from CERN EP-RD program:
  WP5.3: Intelligence on detector, WP5.2: IP blocks, WP5.5: 3D interconnects
  WP6: High Speed links

## Slide 35: Potential Applications of PicoPix
LHCb VELO Upgrade 2 & Fast-Sensor R&D
  High-precision tracking for High-Luminosity LHC (HL-LHC)
  Timing resolution below 50 ps to distinguish multiple collisions
  Radiation-hard hybrid silicon sensors for extreme environments
SY-BI Beam Loss Monitoring
  Bunch-by-bunch beam loss detection
  Improved diagnostics for LHC and future e⁺e⁻ colliders
Medipix3 Collaboration (Medical & Industrial Applications)
  Hadron therapy beam monitoring in cancer treatment
  X-ray diffraction & electron microscopy for material science
  Single-layer Compton cameras for homeland security and SPECT imaging
  Quantum sensing using entangled particle detection

## Slide 36
Pixel Matrix
384 x 256
(pixel size 50mm x 50mm)
Periphery
SPRINT
19.2 mm
12.8 mm
<3.5mm
Picopix Floorplan
SPRINT = Silicon Photonics Radiation-tolerant Integrated Transmitter

## Slide 37: Timing
Target resolution of <20psrms track time is required to distinguish PV
Single plane resolution of <50psrms  σ2sensor (40psrms) + σ2ASIC
σ2ASIC (30psrms) σ2analogFE + σ2conversion + σ2clock
  σ2conversion   TDCbin = 40ps  11.5 psrms
  σ2clock  Reference clock at pixel level < 10 psrms
  σ2analogFE  < 25 psrms

## Slide 38: Fundamental limits to time resolution in analog front-end
R.Ballabriga, The Timepix4 analog front-end design: Lessons learnt on fundamental limits to noise and time resolution in highly segmented hybrid pixel detectors https://doi.org/10.1016/j.nima.2022.167489
  , are the front-end input, feedback, and output capacitances, respectively.
  is the input transconductance
  is the threshold of the comparator
→ Minimize the front-end output capacitance.
→ Increase the analog pixel power consumption, but a large power drop over the ASIC worsens the timing performances!
→ The front-end input capacitance must be minimized, which depends on the choice of the sensor, pixel pitch…
→ Maximize the input charge and decrease the threshold.

## Slide 39
Front-end: Charge Sensitive Amplifier
Front-end: Quenching element, regeneration circuit
Picopix front-end
Notes: A Charge Sensitive Amplifier (CSA) is an electronic circuit designed to convert an input charge (from a sensor or detector) into a proportional voltage output. It is especially common in radiation detection where detectors deliver small charge in response to incident particles.
It presents a low input impedance and a gain (Volts/Charge) which is determined by the inverse of the value of the feedback capacitor (1/CF).

## Slide 40
FULL ASIC
Region
Region
Region
Region
Region
Region
•••
•••
•••
•••
•••
Region
Region
Region
Region
Region
Region
•••
•••
EoC
EoC
EoC
EoC
High speed links
Event sorter and builder
Packet processor
Control
Peri logic
PIXEL
PIXEL
PIXEL
PIXEL
TDC
ARBITRATION
SHARED LOGIC
SUPER-PIXEL
•••
•••
Data manager
Slow-control
Clock distribution logic
digital PLL
PIXEL REGION
Picopix Architecture
2 x 2 pixels
2 x 8 super pixels
96 x 16 pixel regions

## Slide 41: Picopix Time Measurement  1 TDC every 4 pixels
  Free running Digital Control Oscillator
    Period 400ps (2.5GHz)
    UFTOA: ~30-40 ps bin derived from state of inner nodes of VCO
  Auto-calibrated TDC at each measurement:
    P, V, T, Rad and On-chip variations on a large-scale chip are critical for this resolution
  Clock40 designed as an improved precision Timing Clock Tree with Digital DLL (~10 ps clock skew)
  Clock320 used to operate the TDC faster. 1 Measurement in <50ns (Timepix4 was ~300ns)

## Slide 42: On pixel event processing ➞ Data reduction
Data filtered already at the level of the pixel-array
  Bandwidth reduction towards the periphery
  Significant power and IR-drop reduction
Further reduction and compression in the periphery
Arbitration logic (from Medipix3/4)
  Transmit only Master pixel packet (can be disabled)
  ToA on master provide the highest resolution
  Design status: RTL complete
Hit-Map:
  Hit-Map of all the pixels around the master
  Or Hit-Map of the super-pixels around the master (when transmitting all ToT)
  Design status: RTL complete
Advanced on-pixel data filtering:
  ToT range
  ToA range
  Hit-Map shape (single pixel, 2, 2x2,…)
3x3 Veto
5x5 Veto
5x5 is an added mode
Hitmap is always 8bits !

## Slide 43: On pixel event processing ➞ Data reduction
Data filtered already at the level of the pixel-array
  Bandwidth reduction towards the periphery
  Significant power and IR-drop reduction
Further reduction and compression in the periphery
Filtering disable
Filtering large clusters
Filtering small clusters
  Design Status: RTL complete
Clustering and filtering

## Slide 44: Periphery data-path
Full Time calibration:
  DLL clock skew calibration (Row and Column)
  Unique time-walk correction (programable LUT 32x32)
  TOA event calibration (24.4ps bin)
  10b or 6b fine-time output
  Built-in TOA extender up to 32-bits(@40MHz)
  Digital T0Sync shift adjustment (24.4ps bin and 100ns range)
Event Filtering:
  Configurable TOT range
  Configurable TOA range
  Hitmap shape (single pixels, L shape, + shape,…)
On-chip XY decoding
Single packet formatting:
  To Sorter: 24-bit, 36-bit, 72-bit
  To FIFO: 72b_PC_iTOT, 72b_raw and Jumbo
PACKET PROCESSOR

## Slide 45: Picopix operating modes
CLUSTER FILTERING | 
Filter large clusters | Clusters large than 3x3 around master
Filter small clusters | Clusters smaller than 3x3
No filtering | Transmits all clusters
TRACKING MODE | 
Tracking mode | The packet includes: ▪ MASTER ADDRESS ▪ ULTRA-FINE TOA ▪ HIT-MAP
Tracking + ToT | The packet includes: ▪ MASTER ADDRESS ▪ ULTRA-FINE TOA ▪ HIT-MAP ▪ TOT OF ALL THE PIXELS
EVENT PACKET | Tracking mode |  | Tracking mode + ToT | 
 | Packet size | Max N of packets | Packet size | Max N of packets
Raw data format | 72 bits out-of-order | 1.28 GEVENTS s−1 (32 Bx−1) | 144 bits out-of-order | 640 MEVENTS s−1 (16 Bx−1)
Standard format | 36 bits SORTED | 2.56 GEVENTS s−1 (64 Bx−1) | 72 bits SORTED | 1.28 GEVENTS s−1 (32 Bx−1)
Reduced- format | 24 bits SORTED | 3.84 GEVENTS s−1 (96 Bx−1) |  | 
MASTER EXTRACTION | Tracking mode | Tracking mode + ToT
Send cluster master | Full 3X3 Hit-Map around master pixel | Full 3x3 Hit-Map around the super-pixel simplifying the off-chip re-clustering
Send all super-pixels | Local 2x2 Hit-Map within super-pixel | 
Main data-driven readout modes implemented:

## Slide 46
Some personal observations
The success of Timepix4 is based on a collaborative model where institutes agree to fund a generic development
Access to high end and ‘standard vanilla’ CMOS makes this possible and affordable
High volume bump deposition provider reduces bumping costs by almost an order of magnitude. Similarly, TSV processing becomes possible (and relatively cheap) if high volume producers can be found
The old HEP model of 1 (or even multiple) ASICs per sub-detector is dead because of design complexity and engineering run cost.
New funding models (such as proposed by Picopix) show a way forward
However, to reach sustainable solutions in future the HEP community will need to reach out beyond its present silo (as the Medipix Collaborations have done)
https://indico.cern.ch/event/1439855/contributions/6461557/

## Slide 47: Summary and Conclusions
The Timepix family of chips spans 20 years. Each generation provides improved time stamping
Timepix4 can tag hits in bins of 195ps after careful calibration and is 4-side buttable
Picopix implements a number of architectural novelties permitting improved performance and ease of use
  Compatible with various sensors including SPADs
  Improved time stamping (40ps TDC time bin)
  Optional programmable on-pixel data filtering
  Optional on-chip time walk and clock skew correction
  Optional on-chip packet sorting
The HEP community needs to find a new model for working with others to enable future developments

## Slide 48
Thank you for your attention!
Medipix3RX images: S. Procz et al.
Timepix4 paper:
X. Llopart et al 2022 JINST 17 C01044