## Slide 1: Mechanical Design and Integration of the CMS Phase-2 Tracker
Introduction
  CMS
  Tracker
Outer Tracker
  BTST
  TB2S
  TBPS
  TEDD
  ITST
  OT integration in CMS
  Eiffel Tower test
Inner Tracker
  IT integration in CMS
Summary
Original Tracker installation inside CMS (Dec 2007)
Pierre Rose (CERN), on behalf of the CMS Phase 2 Tracker team
VERTEX25 https://indico.phy.ornl.gov/event/677/

## Slide 2: Introduction - CMS
Detector built around a huge solenoid magnet that is superconducting (cooled at -268.5 °C), which generates a magnetic field of 4 Tesla
The different detectors consist of layers of material that exploit the different properties of particles to catch and measure the energy and momentum of each one.
Key features :
  Experience is built 100 m underground Combination of very massive and very light detectors
  High precision and stability requirements in dimensionally large size system High radiation levels
  Low operating temperatures Tons of services (cables, fibres, pipes)
Notes: The detector is built around a huge solenoid magnet. This takes the form of a cylindrical coil of superconducting cable, cooled to -268.5oC, that generates a magnetic field of 4 Tesla, about 100,000 times that of the Earth.
Detectors consist of layers of material that exploit the different properties of particles to catch and measure the energy and momentum of each one. CMS needed:
a high performance system to detect and measure muons,
a high resolution method to detect and measure electrons and photons (an electromagnetic calorimeter),
a high quality central tracking system to give accurate momentum measurements, and
a “hermetic” hadron calorimeter, designed to entirely surround the collision and prevent particles from escaping.
Particles emerging from collisions first meet a tracker, made entirely of silicon, that charts their positions as they move through the detector, allowing us to measure their momentum. Outside the tracker are calorimeters that measure the energy of particles. In measuring the momentum, the tracker should interfere with the particles as little as possible, whereas the calorimeters are specifically designed to stop the particles in their tracks.
The Electromagnetic Calorimeter (ECAL) - made of lead tungstate, a very dense material that produces light when hit – measures the energy of photons and electrons whereas the Hadron Calorimeter (HCAL) is designed principally to detect any particle made up of quarks (the basic building blocks of protons and neutrons). The size of the magnet allows the tracker and calorimeters to be placed inside its coil, resulting in an overall compact detector.
As the name indicates, CMS is also designed to measure muons. The outer part of the detector, the iron magnet “return yoke”, confines the magnetic field and stops all remaining particles except for muons and neutrinos. The muon tracks are measured by four layers of muon detectors that are interleaved with the iron yoke. The neutrinos escape from CMS undetected, although their presence can be indirectly inferred from the “missing transverse energy” in the event.
Within the LHC, bunches of particles collide up to 40 million times per second, so a “trigger” system that saves only potentially interesting events is essential. This reduces the number recorded from one billion to around 100 per second

## Slide 3: Introduction - Tracker
Existing CMS Tracker will be replaced by a completely new one during LS3 for High Luminosity-LHC LS3 will begin in summer 2026 for start HL-LHC in 2030.
Will use new module types capable of selecting high momentum tracks (>2-3 GeV),
-35°C 2-phase CO₂ cooling will be used for cooling down the high-powered electronics
Design focus in lowering material budget
Inner Tracker
Outer Tracker
Particles emerging from collisions first meet a tracker, made entirely of silicon, that charts their positions as they move through the detector, allowing us to measure their momentum
Original Tracker layout
Phase-2 Tracker layout

## Slide 4: Introduction - Tracker
Phase-2 Tracker sub-detectors layout and envelope
BTL : Barrel Timing Layout*
BTST : BTL Tracker Support Tube
ECAL : Electromagnetic Calorimeter*
TB2S : Tracker Barrel with 2S Modules
TEPX : Tracker Endcap Pixel
ITST : Inner Tracker Support Tube
TBPS : Tracker Barrel with PS Modules
TEDD : Tracker Endcap Double Disks
TBPX : Tracker Barrel Pixel
TFPX : Tracker Forward Pixel
* Not covered in this presentation

## Slide 5: Outer Tracker
More Module & Data Acquisition information : Dimitra Andreou talk – Sensor and Module Development for the CMS Phase-2 Tracker Upgrade
Matteo Magherini talk – CMS Tracker Upgrade for Phase-2 : Meeting the Challenges of the HL-LHC
2S (Strip-Strip) Modules
PS (Pixel-Strip) Modules
Phase-2 Outer Tracker layout

## Slide 6: Outer Tracker
Tracker Barrel with PS Modules: 2872 PS Modules
Tracker Barrel with 2S Modules : 4416 2S Modules
Tracker Endcap Double Disks : 5912 PS &2S Modules
Phase-2 Outer Tracker sub-detectors layout

## Slide 7: BTST
Main support structure of the BTL and Tracker
Carbon Fiber sandwich structure with Titanium M16 inserts on the edges and 2 rails inside for sub-detectors installation
Made by a company in the US, first tested at Purdue University and received at CERN in November 2024
Dimension : 5.3 m length, ⌀ 2.5 m
Mass : ≈ 450 kg

## Slide 8: BTST
Heating foils were installed (40 m²), they are used :
  To prevent thermal effects from Tracker (cold) on ECAL (warm)
  To prevent condensation
Defects in the BTST sandwich structure were discovered during the heating foil glueing
Repairs currently on-going
Ultrasonic inspection – Discovery of disbound between structural layers
Repair campaign

## Slide 9: BTST
When BTST will be ready, it will be installed inside its service «cage»
Sub-Tracking detectors will be installed inside the Tube, in CERN clean room called TIF (Tracker Integration Facility)
1st sub-detector to be installed is TB2S
BSTS Service Cage

## Slide 10: Outer Tracker – TB2S
4416 2S (Strip-Strip) Modules
368 Ladders (12 modules per ladder), distributed in 3 layers
1 Wheel carbon structure
Structure mass : 300 kg
Sensor mass : 210 kg
TB2S Wheel structure
TB2S module layers
2S Module

## Slide 11: Outer Tracker – TB2S
2x Bumper
CF Service Support Plate
12x 2S Modules
2x Fork Gate Support
2x Front Sphere Support
BMC Front Panel
2x Mid Sphere Support
2x CF Profiles
13x CF Cross-bars
Titanium Cooling pipe
48x Al inserts
A Ladder consists of a CF frame that provides mechanical and thermal interfaces to the modules and precise location in the wheel
Ladders assembled in Pakistan.

## Slide 12: Outer Tracker – TB2S
Structure made of carbon-fibre composite with aluminium and plastic inserts.
Parts manufacture in companies (IT,FR), assembly in Strasbourg (FR)
Inside the structure, 2 rails are integrated for TBPS installation
Outside, 4 feet are used for holding from BTST
6x Cylinders
4x Disks
TB2S Foot prototype
TB2S CF Disk
TB2S CF Cylinder

## Slide 13: Outer Tracker – TB2S
BTST rail
TB2S support foot
TB2S wheel +
Layer 3 ladders
Extension tool
“Push-pull” tool
TB2S wheel
+ Layer 3 ladders
TB2S/TEDD support frame
BTST & BTL
“Push-pull” tool
TB2S Wheel with L3 ladders will be installed inside BTST with a the “push-pull” tool at TIF
L2 and L1 ladders can be directly installed inside the Wheel from inside BTST (using working platforms)
Then TBPS sub-detector can be inserted

## Slide 14: Outer Tracker – TBPS
2872 PS (Pixel-Strip) Modules
72 TBPS Tilted rings (1920 PS Modules) + 80 Flat planks (952 PS Modules)
Carbon-Fibre structures and supports
Full Tilted TBPS Tilted mass : 220 kg
Full Flat TBPS mass : 45 kg
L1 Tilted section
L1 Flat section
Full TBPS
PS Module
Rings
Beams
Beams
Planks

## Slide 15: Outer Tracker – Flat TBPS
Planks are composed of a Carbon sandwich :
  2 CF plates, Carbon Foam core embedding a cooling pipe.
The Structures and assemblies are made at Fermilab (US)
TBPS Flat structure (without Planks)
TBPS Carbon foam with grooves for pipe
TBPS Plank – Module thermal test

## Slide 16: Outer Tracker – Tilted TBPS
Assembly of the Tilted Rings is occurring at CERN (over 50% of the Rings already produced)
Stacking of the Rings and assembly will occur at TIF
L1 Stacking tool is ready to use
Service layout design is mostly completed
Rings to pass through multiple QC measurements
TBPS L1 Service design
TBPS L2 Ring – 1st produced ring
TBPS L1- Stacking Tool
TBPS Beam assembly

## Slide 17: Outer Tracker – Tilted TBPS – Quality Control
Mass
Metrology
Stiffness
Pressure & Leak Test
Thermal QC Test

## Slide 18: Outer Tracker – TBPS Integration
TBPS Assembly starts with the ITST positioning on the integration tool (ITST described later)
Many steps before TBPS readiness and installation inside the TB2S wheel
The whole assembly will occur at TIF (CERN)
TBPS Assembly tool – 1st step
TBPS completed on its cradle
TBPS insertion inside BTST (inside TB2S)
ITST (central section)

## Slide 19: Outer Tracker – TBPS Integration
BTST
TB2S system axis
(reference)
TB2S detector
TBPS detector +
ITST central section
z
y
x
z
y
x
TBPS system axis
(to be aligned)
x
y
z
x
y
z
TBPS support feet are used to align the two axis systems (adjustable vertically and horizontally)
TB2S rail
When TBPS is well positioned, TEDD sub-detectors can be inserted to complete the Outer Tracker

## Slide 20: Outer Tracker – TEDD
One TEDD : 5 Double-disks, each made of 4 Dees, equipped with both PS & 2S Modules
Dee : 10mm thin sandwich, CF skins and an Airex foam core that houses the cooling pipes
Mass of a whole TEDD : 600 kg
Produced by DESY (DE), Lyon (FR) and Louvain (BE)
Tracker Endcap Double-Dee with Modules
Full TEDD
TEDD – Mechanical Structures

## Slide 21: Outer Tracker – TEDD
Assembly (without silicon modules) of a Tracker Endcap Double Disk (TEDD) with 4 pre-production Dees at the Detector Assembly Facility (DAF) in DESY
Thermal measurement
TEDD – 3D flatness scanning
Cooling Pipes inside a Dee

## Slide 22: Outer Tracker – TEDD
Holding structure, Arc Frame, is used for handling of the Dees during modules and disks integration
The assembly of the Double Disks, to create a TEDD, will take place at TIF (CERN)
The insertion inside BTST of both TEDD also.
TB2S/TEDD support frame
TEDD detector
Temporary support structure for TEDD cables
Arc-Frame with a DD
Assembly tooling at TIF

## Slide 23: Outer Tracker – TEDD Integration
BTST
TEDD system axis
(to be positioned)
TB2S detector
TBPS detector +
ITST central section
z
y
x
z
y
x
TBPS & ITST system axis
(reference)
TEDD detector
TEDD support feet are used to align the two axis systems (adjustable vertically and horizontally)
BTST rail

## Slide 24: Outer Tracker – TEDD - Integration
Bulkhead disk
ITST end section
ITST end section
ITST central section
Bulkhead disk
Bulkhead disk
ITST central section rails
ITST end section rails
ITST end section rails are positioned with respect to those of the ITST central section

## Slide 25: ITST
Inner Tracker Support Tube (ITST) is design to hold and integrate the Inner Tracker sub-detectors
It is fully made and tested in the US (at Purdue University), using carbon fiber composites
Integration and tests campaign are currently performed at Purdue.
Mass < 80 kg
ITST Center Section
ITST End Sections
ITST Center section component production has started
ITST End section component production has started

## Slide 26: Outer Tracker integration in CMS
BTST ready for shipment with the Outer Tracker installed and services wrapped around temporary front end nose cones
Lowering the BTST on the CMS platform (Z-)
Phase-2 BTST
Original– Tracker ready to travel
Original – Tracker with one end services

## Slide 27: Outer Tracker integration in CMS
Phase-2 Tracker will be installed the same way as Phase-1 Tracker in 2007.
For doing this installation, a new push/pull tool has been designed and validated, called Eiffel Tower
The Tracker will be held by 4 Brackets attached to Hadron Calorimeter
Adjustment mechanisms and load instrumentation will be included in the Brackets
BTST insertion sequence (VIDEO)
Original Tracker Insertion
BTST bracket

## Slide 28: Outer Tracker integration in CMS – The “Eiffel Tower” test
Mass : 8000 kg (120% of Tracker mass)
Tests done on surface 2024, the aim was to validate its motion movements.

## Slide 29: Outer Tracker integration in CMS
When the Outer Tracker is correctly positioned inside CMS
The central Beam Pipe will be installed
Then, after BP installation, the Inner Tracker integration in CMS can start.

## Slide 30: Inner Tracker
Tracker Barrel Pixel (TBPX)
  4 layers where 756 Pixel modules are installed
Tracker Forward Pixel (TFPX)
  16 small double disks (8 per end) where 1728 Pixel modules are installed
Tracker Endcap Pixel (TEPX)
  8 doubles disks (4 per end) where 1408 Pixel modules are installed
-35°C 2-phase CO2 cooling (as OT) is used to manage the high-power consumption of the new Pixel modules, and the radiation damage they accumulate over time.
Using as low as possible material in Z to reduce the mechanical impacts for the detector physics performance
More Module & Data Acquisition information : Dimitra Andreou talk – Sensor and Module Development for the CMS Phase-2 Tracker Upgrade
Matteo Magherini talk – CMS Tracker Upgrade for Phase-2 : Meeting the Challenges of the HL-LHC

## Slide 31: Inner Tracker integration in CMS
TFPX and TBPX installation configuration before sliding the quarters inside the ITST
Inner tracker mechanics are made in the US, Italy and Switzerland.
ITST
Bulkhead
Pixel Platform
Temporary rails
TFPX and TBPX quarters
TFPX and TBPX cassettes
Beam pipe

## Slide 32: Inner Tracker integration in CMS
Position clearance from TBPX to the Beam Pipe is only 2mm
Clearance during installation (from all obstacles) is 5mm.
Extension rails
Beam Pipe
Intermediate rails

## Slide 33: Inner Tracker integration in CMS
TEPX installation configuration
The installation occurs after the TFPX-TBPX are positioned inside the ITST
ITST
Bulkhead
TEPX Cassettes
TEPX quarters
Beampipe
TFPX-TBPX

## Slide 34: Inner Tracker integration in CMS
Cut-view of the Inner Tracker installed with services spread on the bulkhead
Outer Tracker (Volume)
Interaction Point
Inner Tracker
Tracker Bracket
Beampipe bellows
Inner Tracker Services
Service Channel
Bulkhead

## Slide 35: Summary – CMS Tracker Phase-2 Mechanics
All mechanical structures (BTST, TB2S, TBPS, TEDD, ITST) are in production worldwide.
Components are meeting precision, stability, thermal, and radiation requirements.
Main Integration tooling (e.g. “Eiffel Tower” push–pull) has been validated.
Production and assembly campaigns are on track for Phase-2 Tracker installation during LS3.

## Slide 36: Spares

## Slide 39
Module Cooling Plate
PS Module
Sandwich Insert (for beam connection)
Cooling Pipe
Sandwich Plate Ring
(cut view)
Core
Skins
TBPS Ring with PS Modules
(cut view)
Module Cooling Plate
Module Cooling Plate
PS Module
Sandwich Plate Ring
Sandwich Insert
Cooling Cap
Cooling Adaptor
Cooling Pipe