## Slide 1: Evaluation of Coded-Aperture Gamma-Ray Imaging for Treaty Accountable Item Characterization
Klaus Ziock
J. Daughhetee
Irakli Garishvili
Frank Gonzalez
Kyle Schmitt

## Slide 2: Verification: What does it mean?
Ideally an inspection conducted under a treaty regime will provide certainty that a Treaty Accountable Item (TAI) is as claimed.
Ideally this means one wants to measure observables directly related to a TAI’s functionality.
Materials
  Isotopics
  Accessible through gamma-ray spectroscopy
Material Distributions
  Shapes
  Dimensions
  Accessible through gamma-ray imaging
But there are sensitivity concerns on these observables
Project Goal: Understand what can be learned/verified from an imaging-based inspection

## Slide 3: Coded-aperture imaging¹
In coded-aperture imaging a shadow mask is used to encode the scene onto a position-sensitive detector.
This allows one to generate images with radiation not amenable to mirrors or lenses.
The image can be recreated using cross-correlation:
¹E.E. Fenimore, T.M. Cannon, Appl Optics, 17, 337, 1978.

## Slide 4: Mask/Anti-Mask Imaging
Image encoded as count-rate variations
Variations not due to the mask cause artifacts
Measure by collecting equal time mask and inverse or anti-mask data
  Use an anti-symmetric mask for this
Removes non-mask background
  Image with both data sets
Provides robust imaging
Provides in situ
background subtraction!

## Slide 5: “Full-deconvolution,” spectrally resolved pixels
Detector
Image
Basic Image generation
Detector can be broken
Into different energy bins
Generate an image in each
Energy bin, then add
Notes: By making an image with each spectral bin, I get a “data-cube” that allows me to generate the spectrum from a given pixel.

## Slide 6: Spectral Region of Interest (sROI)
133Ba 354-358 keV
90-450 keV
232U 237-249 keV
57Co120-124 keV

## Slide 7: Area Region of Interest (aROI)

## Slide 8: Complex Object Imaging
See both radio isotopes and overlying materials
Overlying materials are visible due to scattering of primary radiation

## Slide 9: Spatial Resolution
Can’t see structures smaller than
4, point sources progressively expanded from contact
  Sources ~ 0.4 Resolution elements
  ~ 0.4 Resolution elements
  ~ 1.7 Resolution elements
0.4
0.6
0.8
1.0
1.2
1.5
1.7

## Slide 10: Prior information can provide higher-resolution information
Fits to global shapes can be more precise
Fit
Residual
with:
60 min of data, with uncertainties from bootstrap sampling of events at random
Config. | Block Size (Pixels) | Fit Size (Pixels) |  | Pixels / Block | 
 |  | X | Y | X | Y
2 × 1 | 4.41 | 8.80 | 4.52 | 4.4 ± .028 | 4.52 ± .064
2 × 2 | 4.41 | 8.76 | 8.75 | 4.38 ± .018 | 4.38 ± .018
2 × 2 | 4.44 | 8.73 | 8.76 | 4.37 ± .018 | 4.38 ± .028
But systematic
uncertainties remain
16 Hours

## Slide 11: Bootstrap sample
List mode data represents a reasonable ensemble of what the world throws at the detector
  ~ 1.5 ×108 events
Throw all of the events into a big bucket
pull events out one by one and image
with replacement
Run to desired statistics
1 hour

## Slide 12: Sample Bootstrap Fit Results
Results versus “time”
15 min
7.5 min
30 min
60 min
120 min
X, Y location
X, Y Half Width
Amplitude

## Slide 13: Potential Scenarios: Confirmation of the absence of SNM
Is an object or region free of Special Nuclear Materials (SNM)
  This could be based on detecting gamma-ray emissions: Spectroscopy
Scenario 1: Non-nuclear confirmation
  collect data to verify no gamma emissions
Scenario 2, Sweep “source-free” region
  verify no sources are present in a locale where further work is planned; disassembly, destruction, etc.
Why imaging?
  Allows spectroscopy without a separate background-only measurement.
  Perform near other SNM without concerns about contaminating the measurement.
  The minimum detectable leakage flux allows quantitative determination of how much material could be hidden.
  Direct or down-scattered radiation from a shielded source could be imaged to determine material distribution, serving as a deterrent to cheating.

## Slide 14: Potential Scenarios: Spectral TAI confirmation
Scenario 3: Spectral TAI confirmation
  Use gamma-ray spectroscopy to validate a TAI
  Collect spectra with an imager set so it cannot resolve TAI internal structure
  Intrusiveness concerns with spectroscopy must be addressed
Why Imaging?
  Inherently background-subtracted imaged (aROI) spectra allows such measurements to be performed in proximity to other SNM.
  Imaged spectra (aROI) could allow multiple TAIs to be measured simultaneously.
  Requires:
    Imager spatial resolution treats TAIs as a point source
    TAIs are sufficiently separated to allow non-overlapping aROIs

## Slide 15: Spectroscopic Configurations
Ideal
Ideal Background
Realistic
Realistic Background
Source 2.1 mCi @ 2.3 m, Back Source 10 mCi, @ 2.7 m
Overall Rate 60.7 Hz
Overall Rate 67.5 Hz
Overall Rate 56.1 Hz
Overall Rate 64.4 Hz

## Slide 16: Spectroscopic Configurations
Ideal
Ideal Background
Realistic
5% Signal
10% Signal
15% Signal
20% Signal

## Slide 17: Spectroscopic Configurations
Perturbation
Background
Realistic
0% Signal
5% Signal
10% Signal
15% Signal
20% Signal

## Slide 18: Imaging Configurations
Ideal
Perturbation

## Slide 19: Imaging Configurations
Perturbation
Realistic

## Slide 20: Potential Scenarios: Confirmation a TAI has been altered
Scenario 4: TAI destruction, removal of high explosive
  Validate that low-Z material in proximity to SNM has been removed
Scenario 5: SNM removal
  Validate that SNM has been removed from a TAI
Why Imaging?
  Simultaneous confirmation of both the absence of HE and the TAI-like presence of SNM.
  Confirmatory measurements of the lack of SNM could be performed to a known statistical precision.
  Measurements/work can be performed near other SNM. (e.g. it could be performed at one end of an SNM storage area).

## Slide 21: Potential Scenarios: Confirmation a TAI has been altered
Scenario 6: SNM destruction
  Verify SNM distribution from a TAI has been sufficiently altered to preclude its reuse.
Why Imaging?
  The measurement represents a direct probe as to whether or not a TAI was destroyed.
  New material distribution will likely be less sensitive, allowing the use of higher spatial resolution to discourage cheating.

## Slide 22: Potential Scenarios: Confirmation of a TAI
Scenario 7: TAI confirmation
  Validate that an item is a TAI based on its material distribution
Why Imaging?
  Provides direct confirmation of an attribute related to its material distribution and any relevant declarations
  Template or first principles approach

## Slide 23: Conclusions
Passive gamma-ray imaging can be tailored to provide
  Ruler-verifiable spatial resolution
  Specific spectral resolution (detector-dependent)
  In situ background-subtracted (imaged) spectra
  Quantitative measure of residual source material
These allow inspection scenario classes:
  Confirmation of the absence of SNM
  Spectral TAI confirmation
  Confirmation that a TAI has been altered
  Confirmation of a TAI
Additional research is required to
  Fully understand systematic uncertainties of material distributions
  Automated analysis routines
  Information-barrier technology